## Slide 1: Dynamic Analysis of Cantilever Beam

## Slide 2: Overview
Analytical Solution Details
Solid Rectangular Beam:
  Model dimensions
  Frequency Analysis
  Mode Shapes
  Frequency response
Hollow Rectangular Beam:
  Model dimension
  Frequency Analysis
  Mode Shapes
  Frequency response

## Slide 3: Analytical solution details
ABAQUS results compared to the analytical solution for Euler-Bernoulli beam equation.
Some derivation details provided below.
= 0
Starting with equation below
Assume solution
Applying separation of variables
= 0
Spatial portion solved for eigenfrequencies and shapes
= 0
For the 4th order ODE assume following solution form
And following B.C.’s
Numerically solved for natural frequencies
Plotted for mode shapes

## Slide 4: Solid Rectangular Beam (Dimensions)
Load P = 1000 N
and P = 1000cos(Ωt)
Length L = 1m
X-Section
h = 0.05m
b = 0.05m
Material Properties (Aluminum):
Density = 2711 kg/mm^3
Young’s Modulus = 6.89e10 Pa
Poisson’s Ratio = 0.33
ABAQUS MODEL
Node fixed in translation and rotation
Load applied to end node. Static and dynamic variants
Model Details:
21 node, 20 element beam model
Linear beam element from ABAQUS library (B21)

## Slide 5: Frequency Analysis – Solid Beam
Mode | Analytical (Hz) | FEA (Hz) | % Error
1 | 40.7 | 40.6 | 0.2
2 | 255.2 | 251.5 | 1.4
3 | 714.5 | 691.2 | 3.3
4 | 1400.2 | 1320.3 | 5.7
FEA
Analytical
FEA
Analytical
Analytical
FEA
Analytical
FEA
Lanczos eigensolver used for FEA analysis

## Slide 6: Steady State Dynamic Response – Solid Beam
Analytical Frequency Response Plot
ABAQUS Frequency Response Plot
1
1
Plot notes:
Tip displacement at frequency close to 0 should match static displacement prediction given by , which is calculated to be 9.3mm.
  Analytical = 9.5mm
  FEA = 9.5mm
At 150 Hz have following displacements:
  Analytical = 0.5mm
  FEA = 0.31mm
At 270 Hz have following displacements:
  Analytical = 1.2mm
  FE = 1.6mm
Frequency response measured at the beam tip.
2
2
3
3

## Slide 7: Hollow Rectangular Beam (Dimensions)
Load P = 1000 N
and P = 1000cos(Ωt)
Length L = 1m
X-Section
h = 0.05m
b = 0.05m
Material Properties (Aluminum):
Density = 2711 kg/mm^3
Young’s Modulus = 6.89e10 Pa
Poisson’s Ratio = 0.33
ABAQUS MODEL
Node fixed in translation and rotation
Load applied to end node. Static and dynamic variants
Model Details:
21 node, 20 element beam model
Linear beam element from ABAQUS library (B21)
0.04m

## Slide 8: Frequency Analysis – Hollow Beam
Mode | Analytical (Hz) | FEA (Hz) | % Error
1 | 52.1 | 51.5 | 0.6
2 | 326.8 | 312.6 | 4.3
3 | 915.0 | 834.62 | 8.8
4 | 1793.1 | 1538.4 | 14.2
FEA
Analytical
FEA
Analytical
Analytical
FEA
Analytical
FEA
Lanczos eigensolver used for FEA analysis

## Slide 9: Steady State Dynamic Response – Solid Beam
Analytical Frequency Response Plot
ABAQUS Frequency Response Plot
1
1
Plot notes:
Tip displacement at frequency close to 0 should match static displacement prediction given by , which is calculated to be 15.7mm.
  Analytical = 16.1mm
  FEA = 16.0mm
At 180 Hz have following displacements:
  Analytical = 1mm
  FEA = 0.7mm
At 270 Hz have following displacements:
  Analytical = 2.7mm
  FE = 3.8 mm
Frequency response measured at the beam tip.
2
2
3
3