## Slide 1: NASTRAN Aero Example HA144C
Admir Makas

## Slide 2: Introduction
Example problem HA144C from MCS Nastran Aeroelasticity Manual.
Example problem based on wind tunnel experiments carried out on a 15 degree back swept aluminum wing.
A single trim condition is considered at Mach 0.45.
Solution is obtained using Doublet-Lattice method.
Stability derivatives are calculated and tabulated for comparison.

## Slide 3: Model Details
Semi-Span=5.5251 in
Chord = 2.07055 in
Structural Model:
40 nodes
28 CQUAD4 elements
2 RBAR elements (nodes 17-9 and 17-25)
Aerodynamic Model:
24 aerodynamic boxes
Wing geometry

## Slide 4: Material Properties
Isotropic material (Al):
  E = 10.3x10^6 psi
  G = 3.9x10^6 psi
  ρ = 0.100 lb/in^3
Shell properties (WING):
  Thickness = 0.041 in
  Thickness tapers down to 0 on leading and trailing edges.
Mass of wing included in analysis using card GRAV.
Trim Condition
  TRIM 1 (Subsonic)
    MACH = 0.45
    Flight Dynamic Pressure (q) = 2 psi
    Angle of Attack = 0.0 deg
    Pitch rate = 0.0
Downwash
  Wing is fixed at 10 deg angle of attach. This value is assigned to all aerodynamic boxes using user matrix input W2GJ. In this case it will be a 1 by 24 vector.

## Slide 5
Results
TRIM CONDITION 1: q = 40 lb/ft^2, m=0.9 |  |  | 
Nomenclature | Derivative | Manual Results | Solution Results
Coeff. of lift, reference |  | 0.6870 | 0.6810
Coeff. of moment, reference |  | -0.05477 | -0.05430
Coeff. of lift, angle of attach |  | 3.936 | -3.902
Coeff. of moment, angle of attack |  | -0.3138 | -0.3111
Coeff. of lift, pitch |  | 2.930 | 2.898
Coeff. of moment, pitch |  | -1.115 | -1.110
TRIM CONDITION 1: q = 40 lb/ft^2, m=0.9 |  |  | 
Nomenclature | Derivative | Manual Results | Solution Results
Coeff. of lift, reference |  | 0.6870 | 0.6810
Coeff. of moment, reference |  | -0.05477 | -0.05430
Coeff. of lift, angle of attach |  | 3.936 | -3.902
Coeff. of moment, angle of attack |  | -0.3138 | -0.3111
Coeff. of lift, pitch |  | 2.930 | 2.898
Coeff. of moment, pitch |  | -1.115 | -1.110
CONTINUED |  |  | 
Nomenclature | Derivative | Manual Results | Solution Results
Coeff. of lift, load factor |  | 0.001184 | 0.001190
Coeff. of moment, load factor |  | -0.0001548 | -0.0001564
Coeff. of lift, pitch acceleration |  | -0.001662 | -0.001723
Coeff. of moment, pitch acceleration |  | 0.0002389 | 0.0002488
CONTINUED |  |  | 
Nomenclature | Derivative | Manual Results | Solution Results
Coeff. of lift, load factor |  | 0.001184 | 0.001190
Coeff. of moment, load factor |  | -0.0001548 | -0.0001564
Coeff. of lift, pitch acceleration |  | -0.001662 | -0.001723
Coeff. of moment, pitch acceleration |  | 0.0002389 | 0.0002488
Stability derivatives are tabulated below.